## Slide 1: BARUGO LEVEL III PERFORMANCE REVIEW
MAY 2026

## Slide 2
PRODUCTION - Monthly

## Slide 3
Billed Volume

## Slide 4
PRODUCTION - Daily

## Slide 5
POWER CONSUMPTION

## Slide 6
POWER UNIT USAGE

## Slide 7
ELECTRIC BILL
Month | Chlorination & Intake House Power Consumption (kWh) | LEYECO III based Total Consumption (kWh) | Effective Rate per kWh (PHP) | Electric Bill (PHP)
December 2025 | 4,832.96 | 5,777.00 | ₱11.80 | ₱68,164.36
January 2026 | 6,863.55 | 6,310.00 | ₱14.09 | ₱88,899.61
February 2026 | 5,162.30 | 4,037.00 | ₱11.19 | ₱45,181.15
March 2026 | 4,414.60 | 4,338.00 | ₱13.13 | ₱56,951.04
April 2026 | 5,996.70 | 5,491.00 | ₱11.77 | ₱64,643.84
May 2026 | 7,671.40 | 7,657.00 | ₱10.21 | ₱78,151.73
June 2026 |  |  |  | 
July 2026 |  |  |  | 
August 2026 |  |  |  | 
September 2026 |  |  |  | 
October 2026 |  |  |  | 
November 2026 |  |  |  | 
December 2026 |  |  |  | 
 |  |  | ₱12.03 | ₱401,991.73
 |  |  | Average Rate per kWh | Total Billing

## Slide 8
Unit Usage – Calcium Hypochlorite

## Slide 9
Unit Usage – Hydrogen Peroxide

## Slide 11
Chart: FINANCIAL PANEL
| 46113 | 46143
Intake Bill | 63412.42 | 76584.08
Chlorination Bill | 1231.42 | 1567.65
Intake Facility: Accounted for 98% of the cost increase (Spiked by ₱13,171.66).
Chlorination House: Remained stable and nominal, increasing by only ₱336.23.

## Slide 12
Month | Intake Bill (₱) | Chlorination Bill (₱) | Operating Hours | Production m³ | Specific Energy Consumption (kWh/m³)
April 21, 2026 | ₱ 63,412.42 | ₱ 1,231.42 | 550.5 hrs | 8,542.2 m³ | 0.64 kWh/m³
May 21, 2026 | ₱ 76,584.08 | ₱ 1,567.65 | 608 hrs | 9,813.07 m³ | 0.78 kWh/m³
Chart: OPERATION PERFORMANCE VISUALIZATION
| 46113 | 46143
Production m³ | 8542.2 | 9813.07
Specific Energy Consumption (kWh/m³) | 0.64 | 0.78
Chart: 
| 46113 | 46143
Production m³
Specific Energy Consumption (kWh/m³)
Operating Hours | 550.5 | 608
Chart: OPERATING HOURS
| 46113 | 46143
Production m³
Specific Energy Consumption (kWh/m³)
Trend Line (Operating Hours) | 550.5 | 608
The SEC value tells you exactly how many kilowatts of electricity your plant burns to process one cubic meter (m) of water.

## Slide 13
Month | Intake Bill (₱) | Chlorination Bill (₱) | Operating Hours | Production m³ | Specific Energy Consumption (kWh/m³)
April 21, 2026 | ₱ 63,412.42 | ₱ 1,231.42 | 550.5 hrs | 8,542.2 m³ | 0.64 kWh/m³
May 21, 2026 | ₱ 76,584.08 | ₱ 1,567.65 | 608 hrs | 9,813.07 m³ | 0.78 kWh/m³
Chart: OPERATION PERFORMANCE VISUALIZATION
| 46113 | 46143
Production m³ | 8542.2 | 9813.07
Specific Energy Consumption (kWh/m³) | 0.64 | 0.78
  Water production volume increased by +14.9% (9,813.07 m³).
  Specific Energy Consumption (SEC) spiked by +21.4%, jumping from (0.64 kWh/m³) to (0.78 kWh/m³).
  Average hourly motor load jumped from (9.80 kW) to (12.35 kW) (+26.1%), proving the intake pumps are drawing significantly more current to operate just to move 1 cubic meter.
Chart: 
| 46113 | 46143
Production m³
Specific Energy Consumption (kWh/m³)
Operating Hours | 550.5 | 608
Chart: OPERATING HOURS
| 46113 | 46143
Production m³
Specific Energy Consumption (kWh/m³)
Trend Line (Operating Hours) | 550.5 | 608